## Slide 1: 4diac in Teaching Lessons from Lab Exercises and Student Projects
Martin Melik Merkumians
7th 4diac Users Workshop

## Slide 2: Content
Student background at TU Wiens Electronics Master Programme „Energy and Automation Technology“
Lab course background
Lab exercises
Student project – transportation system
Conclusion

## Slide 3: Student background
Beginner level C skills (no object-orientation)
Beginner level Java skills
Basic Boolean algebra
Basic understanding of finite-state machines (Mealy and Moore)
Introduction to IEC 61131 language und execution model
Introduction to IEC 61499 and its execution model

## Slide 4: Lab course background
Master level course
Focus on automation systems and IEC 61131 / IEC 61499 languages and concepts
Approximately 120-130 students in one semester
Four parts / 4h for each part + preparations at home
  Discrete manufacturing
  Batch process
  Industrial robot (6 axis articulated arm)
  Distributed control with IEC 61499

## Slide 5: Lab exercise – Mechanic Press Example
4diac sample project
Tasks
  Implement control with standard library function blocks only
  Implement a basic function block to control the mechanic press
  Add communication function block for control-to-simulation and control-to-GUI communication
Pros
  Easy to set up
  Provided via 4diac systems
  Distributed scenario (although running on one PC)
  Easy to debug for students
  Suitable for large lab classes (30+ students at once)
Cons
  Simulation only / no hardware specific problems (e.g. Timings, real signal behavior)
  As nothing really happens/moves, students percieve the lab as rather boring

## Slide 6: Lab exercise – Measure and Sort NTC‘s
Gantry robot
Shaker
Sorting station
Measurement
station

## Slide 7: Lab exercise – Measure and Sort NTC‘s

## Slide 8: Lab exercise – Measure and Sort NTC‘s
Lab lecture notes
Description of the plant
Explanation of IEC 61499 and 4diac
30 minute live demonstration of 4diac (Flip-Flop tutorial)
  Basic FB creation and export
  Compile FORTE with new FB
  Test FB with monitoring
Consultation with the lab lecture supervisor (me) and the responsible Student Assistant

## Slide 9: Lab exercise – Measurement Station Control
Turn table in measurement position
Close measurement clamps
Start measurement and readout
Open measurement clamps
Turn table back
Provide measurement to system

## Slide 10: Lab exercise – Overall control
Shake NTC to takeout position
Grab NTC with gantry robot
Put NTC into measurement station
Sort NTC depending on the measurement value

## Slide 11: Lessons learned from first year
Short introduction (30 min) to 4diac IDE/FORTE is not enough for most students to independently create 4diac solutions
Textual explanations of the desired processes are to inaccurate for preparations, even though we tried to be very accurate
The event driven approach of IEC 61499 is hard to grasp for students at first
Basic function block development with ECC and Algorithms is also not always clear to students
FORTE compilation and FB creation should be all done in the same tool

## Slide 12: How to make things better
Four tutorial videos how to install and use 4diac
  Available at (German only) https://www.youtube.com/channel/UCt0MlNo6Y7dXCZSDACXFi1g
Test function blocks, which simulates the plant and gives advice if there are any errors in the desired behavior
Mandatory preparation of the control program
No solution for combining FORTE compilation/FB creation steps

## Slide 13: How 4diac got better through the use in lectures
A lot of bug reports (120 testers per year )
ADS interface FBs for communication with Beckhoff hardware
Added serial interface communication for Windows
Added RawDataLayer for communication
Tutorial videos
Input on how to enhance the ECC and Algorithms views in 4diac-IDE

## Slide 14: Experiences of the second year
Tutorial videos helped a lot!
Setup steps for 4diac IDE and FORTE are a bit to complicated for approximately 30% of students
  Visual Studio changed
  Too much tools (CMake, VS or Cygwin, and 4diac IDE)
Test FBs were very helpful, although they cannot cover all wrong behaviors
4diac IDE has become much more stable

## Slide 15: Transportation system
Platform Festo CPX-CEC
Three different kinds of station types
  2-way junction
  3-way junction
  Handling station
One program for each station
Find shortest path between two stations
Activate path in plant
Communication via MQTT

## Slide 16: Testbed manager

## Slide 17: Feedback to 4diac
Again bug reports
Most important - MQTT communication layer
Able to run FORTE on Festo CPX-CEC (again)
  Can control I/Os and valve ports
  Unfortunately not open source

## Slide 18: Other systems controlled by 4diac
Nutcracker
Platform: Festo CPX-CEC

## Slide 19: Other systems controlled by 4diac
Process plant
Platform: Beckhoff CX5010

## Slide 20: Conclusion
4diac sample projects make it easy to ramp up a course or lab exercise to introduce IEC 61499, but lack reality
Demonstration plants for exercises
  show the complexity and problems of real plants
  are more valued by students
  are a LOT more work to prepare and to use in exercises
Helps to improve 4diac
Are incubators to create new 4diac features