## Slide 1: GNSS-based Regional Ionosphere Modeling
Dzana Halilovic1*, Robert Weber1
* dzana.halilovic@geo.tuwien.ac.at
1 Technical University Vienna, Department of Geodesy and Geoinformation, Vienna, Austria
SGI 2019 Workshop, Berlin, Germany, 26 – 27 September 2019

## Slide 2
Overview
Motivation
Methodology
  Model overview (main characteristics)
  Mapping function and Linear combination
  Processing steps
Analysis
  Validation sites, Output files, Models
  Results and statistics
Conclusions and further work

## Slide 3
WP Technical coordination |  | 
Norvegian Mapping Authority | NMA | NO
WP Participants |  | 
TU Wien (Technical University of Vienna) | TUV | AT
University of Porto | FCUP | PT
Space Research Centre, Polish Academy of Sciences | SRC/CBK | PL
Partnership in the GRC (Galileo Reference Centre) MS Consortium established by the GSA (European GNSS Agency)
Aim of the WP:
  To study and analyze the performance of the NeQuick G ionospheric model in different latitudinal regions
  Comparison to the GPS Klobuchar model
  Evaluation based on data from stations in three latitude regions
Motivation

## Slide 4
High latitudes (above 55° north)
Central European latitudes (TUW region)
Azores and equatorial region
Motivation

## Slide 5
Network: 35 permanent ground stations
Start DoY: 274 (2018)
Grid size: 0.5°x 0.5°
Coverage: +30° to +65° lat -15° to +45° lon
Temporal resolution: 1h (25 maps in file)
Observation type: geometry-free zero-difference code and carrier phase
Sat.system: GPS+Galileo
Integrated electron density: Described by spherical harmonics (up to degree 6)
Software: Bernese v.5.2
  (Post-processing mode)
Methodology: Model overview
Starting DoY with more Galileo data: 182 (2019)
(Galileo contribution increased from 5 to 19 stations)  Quarter 3 to be analyzed after Sept 2019

## Slide 6
MSLM (Modified Single-Layer Model)
All free electrons are concentrated in a shell of infinitesimal thickness at an effective height H (height of maximum electron density at the F2 peak and ranges from 350 km to 450 km.
Methodology: Mapping function
Single-layer model

## Slide 7
Geometry-free linear combination (L4)
Methodology: Linear combination

## Slide 8
Methodology: Processing steps
1. Preparation
Extraction of:
  clock (*.clk)
  pole (*.erp) and
  precise orbit (*.sp3)
  information
Site coordinate extrapolation to current epoch
2. Preprocessing
Code observations screening and smoothing
Rinex files conversion  Bernese formatted file
First SPP solution:
  receiver clock synchronization
Phase observations preprocessing
  cycle slip detection and correction
  outlier detection
3. Processing
Data residual screening (L3)
Outlier identification
Marking identified outliers in observation files
PPP solution
  final site coordinate estimation
Generate ionosphere model (L4)
  station DCB estimation

## Slide 9
Analysis
Sites for validation:
NICO ……………. 30°- 40° lat
AJAC
GRAS ……….. 40°- 50° lat
LEOP
JOZ2 .....……….. 50°- 55° lat
used for DoY 274 (2018) – 90 (2019)
Sites for validation:
NICO ……………. 30°- 40° lat
AJAC
GRAS ……….. 40°- 50° lat
LEOP
WROC .....…….. 50°- 55° lat
used for DoY 91 (2019) -
Output files
Daily VTEC maps for Central Europe
Daily VTEC difference maps for Central Europe w.r.t CODE
Daily site specific range difference plots
Daily site specific residual IONO Slant Error plots
Compared models
TUW regional
NeQuick Gal
GPS Klobuchar
Reference: CODE

## Slide 10
DoY 046 (Q1/2019)
Jan - Mar
Analysis: Results
VTEC maps (TUW regional model)
DoY 135 (Q2/2019)
Apr - Jun

## Slide 11
Analysis: Results
VTEC difference maps for Central Europe w.r.t CODE
DoY 046 (Q1/2019)
DoY 046 (Q1/2019)
DoY 046 (Q1/2019)
TUW regional w.r.t. CODE
Differences up to ~ 4 TECU for this day
NeQuick Gal w.r.t. CODE
Differences up to ~ 8 TECU for this day
GPS Klobuchar w.r.t. CODE
Differences up to ~ 8 TECU for this day

## Slide 12
Analysis: Results
VTEC difference maps for Central Europe w.r.t CODE
DoY 135 (Q2/2019)
DoY 135 (Q2/2019)
DoY 135 (Q2/2019)
TUW regional w.r.t. CODE
Differences up to ~ 3 TECU for this day
NeQuick Gal w.r.t. CODE
Differences up to ~ 7 TECU for this day
GPS Klobuchar w.r.t. CODE
Differences up to ~ 10 TECU for this day

## Slide 13
Analysis: Results
Daily site specific range difference plots (I)
L1+model w.r.t ionosphere-free linear combination (L3)
Mean range difference statistics (%) |  |  | 
Model (%) | <0.5m | <1m | <1.5m
CODE | 66,59 | 88,35 | 95,43
TUW reg. | 62,99 | 86,43 | 94,31
NeQuick G | 35,74 | 62,69 | 83,12
Klobuchar | 38,16 | 64,39 | 80,30
DoY 046 (2019)

## Slide 14
Analysis: Results
Daily site specific range difference plots (II)
L1+model w.r.t ionosphere-free linear combination (L3)
DoY 135 (2019)
Mean range difference statistics (%) |  |  | 
Model (%) | <0.5m | <1m | <1.5m
CODE | 62,66 | 87,26 | 95,78
TUW reg. | 60,47 | 86,77 | 95,59
NeQuick G | 42,12 | 75,75 | 91,65
Klobuchar | 32,09 | 54,22 | 69,08

## Slide 15
Analysis: Results
Daily site specific range difference plots - Statistics
Mean range difference statistics (%) |  |  |  |  |  | 
Model | <0.5m | STD | <1m | STD | <1.5m | STD
CODE | 64,32 | 3,71 | 88,29 | 1,74 | 95,86 | 0,70
TUW reg. | 62,30 | 3,48 | 87,30 | 1,81 | 95,43 | 0,80
NeQuick G | 39,78 | 6,98 | 69,55 | 7,18 | 87,28 | 4,05
Klobuchar | 29,86 | 5,88 | 53,57 | 8,46 | 69,28 | 9,00
DoY 001-181 (2019)

## Slide 16
model
tested value
observation
reference value
Analysis: Results
Daily site specific residual IONO Slant Error plots (I)
Project defined specification
STECREF - STECMOD
2-freq. derived STEC
Model derived STEC
to all visible satellites in all elevation angles

## Slide 17
Analysis: Results
Daily site specific residual IONO Slant Error plots (II)
DoY 046 (2019)
Model | Points outside NeQuickG spec. (%)
CODE | 0,20
TUW reg. | 0,26
NeQuick G | 0,54
STECREF - STECMOD

## Slide 18
Analysis: Results
Daily site specific residual IONO Slant Error plots (III)
DoY 135 (2019)
Model | Points outside NeQuickG spec. (%)
CODE | 0,16
TUW reg. | 0,14
NeQuick G | 0,36
STECREF - STECMOD

## Slide 19
Analysis: Results
Daily site specific residual IONO Slant Error plots - Statistics
Mean IONO slant error statistics | 
Model | Points outside NeQuickG spec. (%)
CODE | 0,19
TUW reg. | 0,19
NeQuick G | 0,59
DoY 001-181 (2019)
Daily mean percentage of epochs outside the NeQuick G specification

## Slide 20
Conclusions
A notable agreement between the TUW regional model and the CODE model, used as a reference (differences up to 5 TECU)
A useful model to provide ionospheric information for single-frequency GNSS users in the European mid-latitude region
Further work
Increased amount of multiGNSS observations in the existing processing included
   First results after September 2019 (for Q3)
Analyze model performance including other satellite systems
Check for stations from other networks (eg. EUREF) to improve model performance on map boundaries
Looking for the next year’s Consortium contract with GSA
Check if our results still match GSA KPIs for this work package

## Slide 21
Thank you for your attention!